## Slide 1: BLM206 Mikroişlemci Sistemleri
M.Aydin - 2018
Chapter 6
Flow Control in Assembly

## Slide 2: Overview
If-then-else
While loop
For loop

## Slide 3: Comparison Instructions
The only effect of the comparisons is to update the condition flags.
  No need to set S bit.
  No need to specify Rd.
Operations are:
  CMP operand1 - operand2, but result not written
  CMN operand1 + operand2, but result not written
  TST operand1 & operand2, but result not written
  TEQ operand1 ^ operand2, but result not written
Examples:
  CMP r0, r1
  TST r2, #5
Instruction | Operands | Brief description | Flags
CMP | Rn, Op2 | Compare | N,Z,C,V
CMN | Rn, Op2 | Compare Negative | N,Z,C,V
TEQ | Rn, Op2 | Test Equivalence | N,Z,C
TST | Rn, Op2 | Test | N,Z,C

## Slide 4: CMP and CMN
CMP{cond} Rn, Operand2
CMN{cond} Rn, Operand2
The CMP instruction subtracts the value of Operand2 from the value in Rn.
  This is the same as a SUBS instruction, except that the result is discarded.
The CMN instruction adds the value of Operand2 to the value in Rn.
  This is the same as an ADDS instruction, except that the result is discarded.
These instructions update the N, Z, C and V flags according to the result.

## Slide 5: Example of CMP
Area absolute, CODE, READONLY
EXPORT __main
ENTRY
__main PROC
CMP r1, #0
RSBLT r0, r1, #0
done B done ; deadloop
ENDP
END
Note: RSB = Reverse SuBtract

## Slide 6: TST and TEQ
TST{cond} Rn, Operand2 ; Bitwise AND
TEQ{cond} Rn, Operand2 ; Bitwise Exclusive OR
The TST instruction performs a bitwise AND operation on the value in Rn and the value of Operand2.
  This is the same as a ANDS instruction, except that the result is discarded.
The TEQ instruction performs a bitwise Exclusive OR operation on the value in Rn and the value of Operand2.
  This is the same as a EORS instruction, except that the result is discarded.
Update the N and Z flags according to the result
Can update the C flag during the calculation of Operand2
Do not affect the V flag.

## Slide 7: Branch Instructions
B label: causes a branch to label.
BL label: instruction copies the address of the next instruction into r14 (lr, the link register), and causes a branch to label.
BX Rm: branch to the address held in Rm
BLX Rm: copies the address of the next instruction into r14 (lr, the link register) and branch to the address held in Rm
Instruction | Operands | Brief description | Flags
B | label | Branch | -
BL | label | Branch with Link | -
BLX | Rm | Branch indirect with Link | -
BX | Rm | Branch indirect | -

## Slide 8: Branch With Link
The "Branch with link (BL)" instruction implements a subroutine call by writing PC-4 into the LR of the current bank.
  i.e. the address of the next instruction following the branch with link (allowing for the pipeline).
To return from subroutine, simply need to restore the PC from the LR:
  MOV pc, lr
  Again, pipeline has to refill before execution continues.
The "Branch" instruction does not affect LR.
Notes: Branch offset must take account of the PC's prefetch offset, which is handled by the assembler
  In effect subtracts 8 before using it : PC normally +8 of what actually executing - pipeline.
The Branch with Link (BL) writes the old PC into the link register (R14) of the current bank.
  Again PC value saved adjusted for the prefetch offset to point to the next instruction after the BL instruction.
    ie saves PC - 4
CPSR has NOT been saved with the PC.
Return using
  MOV pc, lr
Branch Instruction takes 3 cycles because of refilling the pipeline. Similarly on return.

## Slide 9: Condition Codes
Not Equal
Unsigned Higher or Same
Unsigned LOwer
MInus (Negative)
EQual
oVerflow Set
oVerflow Clear
Unsigned HIgher
Unsigned Lower or Same
PLus (Positive or Zero)
Signed Less Than
Signed Greater Than
Signed Less than or Equal
ALways
Signed Greater or Equal
EQ
NE
CS/HS
CC/LO
PL
VS
HI
LS
GE
LT
GT
LE
AL
MI
VC
Suffix
Description
Flags tested
    Note AL is the default and does not need to be specified
Notes:     Condition codes are simply a way of testing the ALU status flags.
    Note AL is the default and does not need to be specified

## Slide 10: Condition Codes
The possible condition codes are listed below:
Not Equal
Unsigned Higher or Same
Unsigned LOwer
MInus (Negative)
EQual
oVerflow Set
oVerflow Clear
Unsigned HIgher
Unsigned Lower or Same
PLus (Positive or Zero)
Signed Less Than
Signed Greater Than
Signed Less than or Equal
ALways
Signed Greater or Equal
EQ
NE
CS/HS
CC/LO
PL
VS
HI
LS
GE
LT
GT
LE
AL
MI
VC
Suffix
Description
Z=0
C=1
C=0
Z=1
Flags tested
N=1
N=0
V=1
V=0
C=1 & Z=0
C=0 or Z=1
N=V
N!=V
Z=0 & N=V
Z=1 or N!=V
    Note AL is the default and does not need to be specified
Notes:     Condition codes are simply a way of testing the ALU status flags.
    Note AL is the default and does not need to be specified

## Slide 11: Signed Greater or Equal ( N == V)
 | N = 0 | N = 1
V = 0 | No overflow, implying the result is correct. The result is non-negative, Thus r0 – r1 ≥ 0, i.e., r0 ≥ r1 | No overflow, implying the result is correct. The result is negative. Thus r0 – r1 < 0, i.e., r0 < r1
V = 1 | Overflow occurs, implying the result is incorrect. The result is mistakenly reported as non-negative and in fact it should be negative. Thus r0 – r1 < 0 in reality, i.e., r0 < r1 | Overflow occurs, implying the result is incorrect. The result is mistakenly reported as negative and in fact it should be non-negative. Thus r0 – r1 ≥ 0 in reality., i.e. r0 ≥ r1
CMP r0, r1
We in fact perform subtraction r0 – r1, without saving the result.
Conclusions:
If N == V, then it is signed greater or equal (GE).
Otherwise, it is signed less than (LT)

## Slide 12: Signed vs. Unsigned
Compare | Signed | Unsigned
== | EQ | EQ
≠ | NE | NE
> | GT | HI
≥ | GE | HS
< | LT | LO
≤ | LE | LS
Compare | Signed | Unsigned
== | BEQ | BEQ
!= | BNE | BNE
> | BGT | BHI
>= | BGE | BHS
< | BLT | BLO
<= | BLE | BLS
Conditional codes applied to branch instructions

## Slide 13: Branch Instructions
 | Instruction | Description | Flags tested
Unconditional Branch | B label | Branch to label | 
Conditional Branch | BEQ label | Branch if EQual | Z = 1
 | BNE label | Branch if Not Equal | Z = 0
 | BCS/BHS label | Branch if unsigned Higher or Same | C = 1
 | BCC/BLO label | Branch if unsigned LOwer | C = 0
 | BMI label | Branch if MInus (Negative) | N = 1
 | BPL label | Branch if PLus (Positive or Zero) | N = 0
 | BVS label | Branch if oVerflow Set | V = 1
 | BVC label | Branch if oVerflow Clear | V = 0
 | BHI label | Branch if unsigned HIgher | C = 1 & Z = 0
 | BLS label | Branch if unsigned Lower or Same | C = 0 or Z = 1
 | BGE label | Branch if signed Greater or Equal | N = V
 | BLT label | Branch if signed Less Than | N != V
 | BGT label | Branch if signed Greater Than | Z = 0 & N = V
 | BLE label | Branch if signed Less than or Equal | Z = 1 or N = !V

## Slide 14: Number Interpretation
If they represent signed numbers, the latter is greater
(1 > -1).
If they represent unsigned numbers, the former is greater
(4294967295 > 1).
Which is greater?
0xFFFFFFFF or 0x00000001

## Slide 15: Which is Greater: 0xFFFFFFFF or 0x00000001?
signed int x, y ; x = -1;
y = 1; if (x > y)
...
unsigned int x, y ;
x = 4294967295;
y = 1;
if (x > y)
...
BLE: Branch if less than or equal, signed ≤
BLS: Branch if lower or same, unsigned ≤
It’s software’s responsibility to tell computer how to interpret data:
If written in C, declare the signed vs unsigned variable
If written in Assembly, use signed vs unsigned branch instructions
MOVS r6, #0xFFFFFFFF MOVS r5, #0x00000001
CMP r5, r6 BLE Then_Clause
...
MOVS r6, #0xFFFFFFFF MOVS r5, #0x00000001
CMP r5, r6 BLS Then_Clause
...

## Slide 16: If-then Statement
C Program
if (a < 0 ) { a = 0 – a; } x = x + 1;
; r1 = a, r2 = x
CMP r1, #0 ; Compare a with 0
BGE endif ; Go to endif if a ≥ 0
then RSB r1, r1, #0 ; a = - a
endif ADD r2, r2, #1 ; x = x + 1
Implementation 1:

## Slide 17: If-then Statement
C Program
if (a < 0 ) { a = 0 – a; } x = x + 1;
; r1 = a, r2 = x
CMP r1, #0 ; Compare a with 0
RSBLT r1, r1, #0 ; a = 0 - a if a < 0
ADD r2, r2, #1 ; x = x + 1
Implementation 2:

## Slide 18: Compound Boolean Expression
x > 20 && x < 25
x == 20 || x == 25
!(x == 20 || x == 25)
C Program | Assembly Program
// x is a signed integer if(x <= 20 ¦¦ x >= 25){ a = 1 } | ; r0 = x CMP r0, #20 ; compare x and 20 BLE then ; go to then if x ≤ 20 CMP r0, #25 ; compare x and 25 BLT endif ; go to endif if x < 25 then MOV r1, #1 ; a = 1 endif

## Slide 19: If-then-else
C Program
if (a == 1) b = 3; else b = 4;
; r1 = a, r2 = b
CMP r1, #1 ; compare a and 1
BNE else ; go to else if a ≠ 1
then MOV r2, #3 ; b = 3
B endif ; go to endif
else MOV r2, #4 ; b = 4
endif

## Slide 20: For Loop
C Program
int i; int sum = 0; for(i = 0; i < 10; i++){ sum += i; }
MOV r0, #0 ; i
MOV r1, #0 ; sum
B check
loop ADD r1, r1, r0
ADD r0, r0, #1
check CMP r0, #10
BLT loop
endloop
Implementation 1:

## Slide 21: For Loop
C Program
int i; int sum = 0; for(i = 0; i < 10; i++){ sum += i; }
MOV r0, #0 ; i
MOV r1, #0 ; sum
loop CMP r0, #10
BGE endloop
ADD r1, r1, r0
ADD r0, r0, #1
B loop
endloop
Implementation 2:

## Slide 22: Combined Program Status Registers (xPSR)
Notes: The Q flag is sticky in that, when set to 1 by an instruction, it remains set until explicitly cleared to 0 by an MSR instruction writing to the CPSR. Instructions cannot execute conditionally on the status of the Q flag.
Saturation arithmetic is a version of arithmetic in which all operations such as addition and multiplication are limited to a fixed range between a minimum and maximum value. If the result of an operation is greater than the maximum it is set ("clamped") to the maximum, while if it is below the minimum it is clamped to the minimum. The name comes from how the value becomes "saturated" once it reaches the extreme values; further additions to a maximum or subtractions from a minimum will not change the result.
For example, if the valid range of values is from -100 to 100, the following operations produce the following values:
60 + 43 = 100
(60 + 43) − 150 = −50
43 − 150 = −100
60 + (43 − 150) = −40
10 × 11 = 100
99 × 99 = 100
30 × (5 − 1) = 100
30×5 − 30×1 = 70
Green psr bits are only in certain versions of the ARM architecture
ALU status flags (set if "S" bit set, implied in Thumb state).
Sticky overflow flag (Q flag) is set either when
  saturation occurs during QADD, QDADD, QSUB or QDSUB, or
  the result of SMLAxy or SMLAWx overflows 32-bits
Once flag has been set can not be modified by one of the above instructions and must write to CPSR using MSR instruction to cleared
PSRs split into four 8-bit fields that can be individually written:
Control (c) bits 0-7
Extension (x) bits 8-15 Reserved for future use
Status (s) bits 16-23 Reserved for future use
Flags (f) bits 24-31
Bits that are reserved for future use should not be modified by current software. Typically, a read-modify-write strategy should be used to update the value of a status register to ensure future compatibility. Note that the T/J bits in the CPSR should never be changed directly by writing to the PSR (use the BX/BXJ instruction to change state instead).
However, in cases where the processor state is known in advance (e.g. on reset, following an interrupt, or some other exception), an immediate value may be written directly into the status registers, to change only specific bits (e.g. to change mode).
New ARM V6 bits now shown.

## Slide 23: Combined Program Status Registers (xPSR)
N
Z
C
V
ISR number
Reserved
Reserved
ICI/IT
Reserved
T
Reserved
ISR number
Application PSR
(APSR)
Interrupt PSR
(IPSR)
Execution PSR (PSR)
Combined PSR (xPSR)
bit0
bit8
bit16
bit24
bit31
Q
ICI/IT
T
N
Z
C
V
Q
ICI/IT
ICI/IT

## Slide 24: Condition Codes
The possible condition codes are listed below:
Not equal
Unsigned higher or same
Unsigned lower
Negative
Equal
Overflow
No overflow
Unsigned higher
Unsigned lower or same
Positive or Zero
Signed Less than
Signed Greater than
Signed Less than or equal
Always
Signed Greater or equal
EQ
NE
CS/HS
CC/LO
PL
VS
HI
LS
GE
LT
GT
LE
AL
MI
VC
Suffix
Description
Z=0
C=1
C=0
Z=1
Flags tested
N=1
N=0
V=1
V=0
C=1 & Z=0
C=0 or Z=1
N=V
N!=V
Z=0 & N=V
Z=1 or N!=V
    Note AL is the default and does not need to be specified
Notes:     Condition codes are simply a way of testing the ALU status flags.
    Note AL is the default and does not need to be specified

## Slide 25: Conditional Execution
Add instruction | Condition | Flag tested
ADDEQ r3, r2, r1 | Add if EQual | Add if Z = 1
ADDNE r3, r2, r1 | Add if Not Equal | Add if Z = 0
ADDHS r3, r2, r1 | Add if Unsigned Higher or Same | Add if C = 1
ADDLO r3, r2, r1 | Add if Unsigned LOwer | Add if C = 0
ADDMI r3, r2, r1 | Add if Minus (Negative) | Add if N = 1
ADDPL r3, r2, r1 | Add if PLus (Positive or Zero) | Add if N = 0
ADDVS r3, r2, r1 | Add if oVerflow Set | Add if V = 1
ADDVC r3, r2, r1 | Add if oVerflow Clear | Add if V = 0
ADDHI r3, r2, r1 | Add if Unsigned HIgher | Add if C = 1 & Z = 0
ADDLS r3, r2, r1 | Add if Unsigned Lower or Same | Add if C = 0 or Z = 1
ADDGE r3, r2, r1 | Add if Signed Greater or Equal | Add if N = V
ADDLT r3, r2, r1 | Add if Signed Less Than | Add if N != V
ADDGT r3, r2, r1 | Add if Signed Greater Than | Add if Z = 0 & N = V
ADDLE r3, r2, r1 | Add if Signed Less than or Equal | Add if Z = 1 or N = !V

## Slide 26: Example of Conditional Execution
if (a <= 0)
y = -1;
else
y = 1;
CMP r0, #0
MOVLE r1, #-1
MOVGT r1, #1
LE: Signed Less than or Equal
GT: Signed Greater Than
a ⟶ r0
y ⟶ r1
Notes: Sequence of conditional instructions:
- no instruction must reset cond code flags
- BL corrupts flags so must be last
- limit sequence to max 3 or so instrs
Can use different condition codes. Give if then else example. Note GCD practical coming later.
Conditional compare
- resets condition code when executed
- compiler will make use of this
- can be difficult for a human to understand!
Not just for compare, using data processing with condition code and S bit is useful in some circumstances.
LDM/LDR instruction cannot set flags due to datapath issues (data comes back only at the very end of the cycle, so there is no opportunity to perform a comparison and set the status flags).

## Slide 27: Example of Conditional Execution
if (a==1 || a==7 || a==11)
y = 1;
else
y = -1;
CMP r0, #1
CMPNE r0, #7
CMPNE r0, #11
MOVEQ r1, #1
MOVNE r1, #-1
NE: Not Equal
EQ: Equal
a ⟶ r0
y ⟶ r1
Notes: Sequence of conditional instructions:
- no instruction must reset cond code flags
- BL corrupts flags so must be last
- limit sequence to max 3 or so instrs
Can use different condition codes. Give if then else example. Note GCD practical coming later.
Conditional compare
- resets condition code when executed
- compiler will make use of this
- can be difficult for a human to understand!
Not just for compare, using data processing with condition code and S bit is useful in some circumstances.
LDM/LDR instruction cannot set flags due to datapath issues (data comes back only at the very end of the cycle, so there is no opportunity to perform a comparison and set the status flags).

## Slide 28: Compound Boolean Expression
C Program | Assembly Program
// x is a signed integer if(x <= 20 ¦¦ x >= 25){ a = 1; } | ; r0 = x, r1 = a CMP r0, #20 ; compare x and 20 MOVLE r1, #1 ; a=1 if less or equal CMP r0, #25 ; CMP if greater than MOVGE r1, #1 ; a=1 if greater or equal endif

## Slide 29: Example 1: Greatest Common Divider (GCD)
While (a != b ) {
if (a > b) a = a – b;
else b = b – a;
}
; suppose r0 = a and r1 = b
gcd CMP r0, r1 ; a > b?
BEQ end ; if a = b, done
BLT less ; a < b
SUB r0, r0, r1 ; a = a – b
B gcd
less SUB r1, r1, r0 ; b = b – a
B gcd
Euclid’s Algorithm
gcd CMP r0, r1
SUBGT r0, r0, r1
SUBLT r1, r1, r0
BNE gcd

## Slide 30: Example 2
int foo(int x, int y) {
if ( x + y < 0 )
return 0;
else
return 1;
}
foo ADDS r0, r0, r1
BPL PosOrZ
done MOV r0, #0
MOV pc, lr
PosOrZ MOV r0, r1
B done
foo ADDS r0, r0, r1 ; r1 = x + y, setting CCs
MOVPL r0, #1 ; return 1 if n bit = 0
MOVMI r0, #0 ; return 0 if n bit = 1
MOV pc, lr ; exit foo function

## Slide 31: Combination
Except that it does not change the condition code flags, CBZ Rn, label is equivalent to:
  CMP Rn, #0
  BEQ label
Except that it does not change the condition code flags, CBNZ Rn, label is equivalent to:
  CMP Rn, #0
  BNE label
Instruction | Operands | Brief description | Flags
CBZ | Rn, label | Compare and Branch if Zero | -
CBNZ | Rn, label | Compare and Branch if Non Zero | -

## Slide 32: Break and Continue
Example code for break | Example code for continue
for(int i = 0; i < 5; i++){ if (i == 2) break; printf(“%d, ”, i) } | for(int i = 0; i < 5; i++){ if (i == 2) continue; printf(“%d, ”, i) }
Output: ?? | Output: ??

## Slide 33: Break and Continue
Example code for break | Example code for continue
for(int i = 0; i < 5; i++){ if (i == 2) break; printf(“%d, ”, i) } | for(int i = 0; i < 5; i++){ if (i == 2) continue; printf(“%d, ”, i) }
Output: 0, 1, | Output: 0, 1, 3, 4

## Slide 34: Break and Continue
C Program | Assembly Program
// Find string length char str[] = "hello"; int len = 0; for( ; ; ) { if (*str == '\0') break; str++; len++; } | ; r0 = string memory address ; r1 = string length MOV r1, #0 ; len = 0 loop LDRB r2, [r1] CBNZ r2, notZero B endloop notZero ADD r0, r0, #1 ; str++ ADD r1, r1, #1 ; len++ B loop endloop

## Slide 35: IT (If-Then) instruction
IT{x{y{z}}} {cond}
where the x, y, and z specify the existence of the optional second, third, and fourth conditional instruction respectively.
x, y, and z are either T (Then) or E (Else)
ITTE NE ; IT can be omitted
ANDNE r0,r0,r1 ; 16-bit AND, not ANDS
ADDNE r2,r2,#1 ; 32-bit ADDS
MOVEQ r2,r3 ; 16-bit MOV
ITT AL ; emit 2 non-flag setting 16-bit instructions
ADDAL r0,r0,r1 ; 16-bit ADD, not ADDS
SUBAL r2,r2,#1 ; 16-bit SUB, not SUB
ADD r0,r0,r1 ; expands into 32-bit ADD, and is not in IT block
ITT EQ
MOVEQ r0,r1
BEQ dloop ; branch at end of IT block is permitted
ITT EQ
MOVEQ r0,r1
ADDEQ r0,r0,#1
Examples:

## Slide 36: IT (If-Then) instruction
You do not need to write IT instructions in your code.
The assembler generates them for you automatically according to the conditions specified.
IT{x{y{z}}} {cond}
where the x, y, and z specify the existence of the optional second, third, and fourth conditional instruction respectively.
x, y, and z are either T (Then) or E (Else)

## Slide 37: Branch Instructions
B label: causes a branch to label.
BL label: instruction copies the address of the next instruction into r14 (lr, the link register), and causes a branch to label.
BX Rm: branch to the address held in Rm
BLX Rm: copies the address of the next instruction into r14 (lr, the link register) and branch to the address held in Rm
Instruction | Operands | Brief description | Flags
B | label | Branch | -
BL | label | Branch with Link | -
BLX | Rm | Branch indirect with Link | -
BX | Rm | Branch indirect | -

## Slide 38
Reference:
Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C
Dr. Yifeng Zhu Electrical and Computer Engineering University of Maine